Continuous Mandatory Ventilation Controller
Project 2019

---
Deep Sleep Mode
2019-03-22 21:54
uC active : > 30 mA
Deep sleep : 5.7 mA
Deep sleep w/o sensor : 5.7 mA
Deep sleep w/o sensor & RF : 4.5 mA
pin	description
1	NC
2	GPIO16
3	RST
Quiescent
Current 5 mA!
Deep sleep
mode activated

---
User LED
1.9V
ESP8266
GPIO5
5V

---
RF433 Connector
pin	description
1	5V
2	key
3	NC
4	GPIO14 (data)
5	GND
Board
RF433

---
DHT22 Connector
pin	description
1	3.3V
2	GPIO12
3	key
4	key
5	GND
Board
Sensor
DHT22

---
Electrical Connection
220V
220V
CMV Controller
433 MHz
433 MHz
Interruptor
CMV Motor
Triple
Interruptor
DIO
++++
++
Neutral
N
    N

---
Annex. ESP8266 pinout